## Slide 1
Particle Board Manufacture

## Slide 2
Essentially, particleboard (sometimes referred to as ‘chipboard’) is a type of manufactured wood made from compressed wood particles. It is made from a combination of post recycled consumer wood – such as planer shavings, offcuts or sawdust –mixed with resin which are formed into boards by curing in a heat press.
General Description

## Slide 3
Collection of raw materials
Roundwood logs are brought in by lorry from surrounding forests
Recycled wood is also brought in
Saw dust from local sawmills
Particle Board Manufacture

## Slide 4
Preparation of recycled wood
The roundwood logs are fed into a machine to remove bark and any grit/sand stuck to it
Logs are fed into the flaker machine and are shaved or cut to make wood flakes, chips and shavings
Particle Board Manufacture

## Slide 5
Preparation of roundwood logs
The recycled wood is fed into Mill, which smashes the wood into woodchips with revolving metal hammers and discards all other waste products
Woodchips are passed up a conveyor and the metal, plastics and rags removed from the woodchips. A large magnet is used to remove the metal
Particle Board Manufacture

## Slide 6
Drying chips
Woodchips from the recycled timber and logs are dried in a big drum by hot air produced from burning the very fine waste wood dust
Removes the pollutants and dust from the wood drying process
Birds eye view into the burning chamber which creates the heat to dry the wood chips
Particle Board Manufacture

## Slide 7
Mixing chips with synthetic resin
The wood chips are now mixed with glue and wax. The glue is used to bond the chips together and the wax makes the chipboard water resistant
Particle Board Manufacture

## Slide 8
Pressing chips
The wood chips are now ready for pressing and are fed into a forming station and then into a conveyor belt called a forming line
Particle Board Manufacture

## Slide 9
Applying heat to press
From the forming line the chipboard moves to a pressing plant where the moisture is driven off and board is pressed at high temperature and pressure in the main process.
Particle Board Manufacture

## Slide 10
Dimensioning
The edges of the board are trimmed and the board cut into large panels before being cooled, sanded and packed for storage in the warehouse.
Particle Board Manufacture